## Slide 1
PROGRESS UPDATE
How Sensitive Is On-Time
Performance to
Measurement Choices?
A Robustness Protocol for Public Transit KPIs
Tobias Bussiek
April 2026
Notes: (~30 seconds) "Today I'm presenting my research proposal for this semester. It's centered on public transit performance measurement — specifically, on a problem that I think is more serious than it looks on the surface. The core question is: when an agency publishes an on-time performance number, how much should we actually trust it?"

## Slide 2
MOTIVATION
SEPTA says a bus is on time if it's within 5 minutes of schedule. What if that window were 3 minutes? What if they only measured at certain stops?
The number changes each time — but it's reported as a single fact.
1
Opaque numbers
Agencies report OTP as one clean figure, hiding the definitional choices behind it.
2
Incomparable metrics
Two agencies both report "OTP" but measure it differently — comparisons are meaningless.
3
No sensitivity standard
Transit agencies do not appear to use a standard protocol for reporting how sensitive their KPIs are to definition choices.
Notes: (~1 minute) "Let me start with why this matters. SEPTA — Philadelphia's transit authority — defines a bus as on-time if it arrives within 5 minutes of schedule. But what if that window were 3 minutes? The number changes. What if they only measured at certain stops? Changes again. What if canceled trips counted as late instead of being excluded? Changes again. None of those choices are wrong — they're all defensible. But they produce different numbers, and those numbers get reported publicly as precise facts. This creates three concrete problems..." [Point to cards — keep it brief, the cards speak for themselves]

## Slide 3
DATA & CURRENT STATUS
Current Progress
DATA SOURCES
SEPTA GTFS Static
Routes 23 & 47, weekday service, April 2026
SEPTA GTFS-RT
Bus trip updates, self-archived since April 4th — SEPTA publishes no historical data
Analysis to date
April 7th used as proof of concept — full multi-week rerun before May submission
EARLY RESULTS
OTP ranged from 49% to 95%
same buses · same day · different definitions
Route Strict (0–3) Standard (−1 to +5) Lenient (−2 to +7)
Rt 23 49.2% 85.9% 94.5%
Rt 47 44.3% 79.8% 91.3%
Threshold alone drives a 45pp swing on Route 23
Phase 2 complete — current results from 1 weekday (Apr 7). Full analysis will use 3–4 weeks of weekday data collected by May.
Notes: (~1 minute) "In terms of where things stand — this is already running. I have the GTFS static schedule downloaded — about 2.4 million rows across 42,000 trips. More importantly, I have a live archiver polling SEPTA's bus feed every 60 seconds and storing timestamped snapshots. SEPTA doesn't publish historical real-time data, so if I hadn't started collecting this now, I'd have nothing to analyze later. The infrastructure is in place. The next step is to scope down to 2 or 3 specific bus routes and formally define the specification set."

## Slide 4
TIMELINE & RISKS
NOW
Phase 1
Scope + Static
Analysis
✓ Routes 23 & 47 selected
✓ Initial Spec set defined (5 dimensions)
✓ Headways + schedules explored
DONE
Phase 2
Parse
GTFS-RT
✓ Decoded GTFS-RT protobuf
✓ Matched trips to schedule
✓ First OTP results computed
Phase 3
Compute &
Compare
→ More data (2+ weeks)
→ Driver variance analysis + more Specs
→ Power BI dashboard
FINAL
Phase 4
Results
+ Paper
→ Formulate findings
→ Reporting template
→ Reproducible repo
KEY CHALLENGES RESOLVED
DONE
Phase 1
Phase 3
Timezone offset resolved
GTFS-RT timestamps are UTC; scheduled times are Eastern. Undetected, this produces 250-min delays on every bus — the kind of error that would silently invalidate a published analysis.
5 specification dimensions implemented
Lateness threshold · Early departure treatment · Stop selection · Time of day · Stop position in route
Pipeline fully reproducible
4 notebooks, DuckDB + Python, DigitalOcean archiver. Rerunning on full dataset requires changing one date filter — everything else is automated.
Notes: (~1.5 minutes) "I've broken the semester into four phases. Right now I'm in Phase 1 — scoping routes and analyzing the static schedule. Phase 2 is parsing the real-time feeds and matching trips. Phase 3 is the core robustness analysis. Phase 4 is the dashboard and paper. The sequencing is intentional — I want to fully understand the static data before touching real-time parsing, because that's where the complexity lives. Let me also flag three risks I'm watching. First, SEPTA doesn't archive real-time data, so I'm self-archiving from week 1. Second, GTFS-RT gives predictions, not ground truth — I'm handling that by defining two separate KPI families. Third, scope — the research document describes seven KPIs. I'm starting with OTP only and expanding to headway metrics only if time permits."

## Slide 5
EARLY FINDINGS
Research questions
RQ1: Route 23 OTP ranges from 49.2% to 94.5% — a 45pp spread — across three
reasonable lateness threshold definitions. Route 47 shows a similar 47pp spread.
RQ2: Lateness threshold (45pp) and early departure treatment (40pp) drive the most variance. Stop selection barely matters (2pp). Time of day matters for Route 47 (21pp PM peak gap).
Sensitivity Analysis
Route 23: 49.2% → 94.5% OTP across threshold definitions. Route 47: 44.2% → 91.3%. Same data, same buses.
Driver Identification
Threshold and early-departure rules dominate. Stop selection (timepoints vs all) contributes only 2pp — smaller than expected.
Reporting Standard
Any agency publishing OTP must disclose threshold, early-departure rule, and time-of-day scope. These three choices alone explain most of the variance.
Pipeline: 4 notebooks · DuckDB + Python · DigitalOcean archiver · GitHub: tobibussiek/TransitKPIFramework
Thank you — happy to take questions.
Notes: (~45 seconds) "Let me close with the expected contribution, stated as clearly as I can. The research questions are on screen. First: how much does OTP actually move when you vary reasonable preprocessing choices? Second: which choices drive the most variation? The contribution has three parts. A sensitivity analysis showing how much OTP shifts under defensible specifications. An identification of which decisions — threshold, stop selection, cancellations — matter most. And a proposed minimum reporting standard so that any agency publishing a KPI can document its sensitivity range. The pipeline, dashboard, and protocol checklist support that — they're the artifacts, not the finding. Thank you. Happy to take questions."