## Slide 1
FINAL RESULTS
KPI Robustness in
On-Time Performance
Measurement
How sensitive is OTP to defensible methodological choices?
Tobias Bussiek
West Chester University of Pennsylvania
April 2026
Notes: Hi everyone. I’m Tobi. This is the final results presentation for my final project: KPI Robustness in On-Time Performance Measurement.
The question I’m asking is pretty simple: when a transit agency or analyst tells you a bus route is, say, 75 percent on time, how much does that number depend on the choices someone made to compute it?
The answer is: a lot more than I expected.
[next slide]
1

## Slide 2
THE PROBLEM
OTP is reported as a single percentage.
But computing OTP from public GTFS-RT data requires methodological choices
and reasonable choices produce dramatically different numbers.
1
Hidden choices
Computing OTP from GTFS-RT requires picking lateness windows, handling early arrivals, selecting stops, and deduplicating overlapping real-time predictions.
2
Invisible upstream
Some choices are recognizable as methodology (e.g., the 5-minute window). Others happen earlier, during stop-event reconstruction, and rarely appear in published reports.
3
Same data, different number
Across reasonable choices, the same underlying data can be reported as 20% on-time, 99% on-time, or anywhere in between. The reader cannot tell which methodology produced the number.
Notes: Here’s the setup.
Transit agencies publish on-time performance numbers all the time. SEPTA, the MTA in New York, Metra in Chicago — they all report OTP as a single clean percentage on a dashboard somewhere.
But if you’re an outside analyst — a researcher, a journalist, or someone at a watchdog group — and you want to compute OTP yourself from public real-time data, you have to make a lot of methodological choices first.
Some are obvious. What counts as on time — three minutes late? Five minutes late? Some are less obvious: how do you handle early arrivals? Which stops do you measure at?
And then there are choices that happen even earlier in the pipeline, before the OTP definition is even applied.
The result is what you see on the slide: hidden choices, upstream reconstruction decisions, and the same data producing dramatically different numbers depending on the method.
[next slide]
2

## Slide 3
WHERE THE CHOICES LIVE
GTFS-RT pipeline choices are part of KPI methodology
Each step in reconstructing a stop event from real-time predictions involves a methodological choice.
STEP 1
Archive feed
Poll GTFS-RT every
60 seconds
>
STEP 2
Match to schedule
Trip ID + stop
sequence
>
STEP 3
Assign service date
Rolling 4 AM Eastern
boundary
>
STEP 4
Reconstruct stop event
Pick which prediction
represents the stop
>
STEP 5
Apply OTP definition
Lateness window,
early treatment
STEP 4 GETS MUCH LESS ATTENTION
Snapshot selection: which prediction represents the stop event?
GTFS-RT is a stream of overlapping live predictions, not a finished historical record.
A single scheduled stop appears in many snapshots as the bus approaches. The analyst must pick one.
This study compares three rules: closest (prediction nearest scheduled time), last_before (last prediction before scheduled time), and latest (chronologically last, treated here as the closest GTFS-RT-only proxy).
Notes: This is the conceptual core of the project.
When you compute OTP from public GTFS-RT data — that’s the standard real-time transit feed format — you go through these five steps.
You archive the live feed. You match the real-time updates to the static schedule. You assign each event to a service date, which is trickier than it sounds because some bus trips cross midnight. You reconstruct the stop event. And finally, you apply the OTP definition.
The literature on OTP definitions has been around for years. Lateness windows, stop selection, how to handle early arrivals — those are the choices people usually discuss. Those mostly live in step five.
But step four gets much less attention.
Here’s why it matters. GTFS-RT is not a finished historical record. It is a stream of live predictions. As a bus approaches a stop, the feed updates the predicted arrival time over and over. So for one scheduled stop event, you may have many different predictions.
Which one represents the stop? You have to pick. That choice — the snapshot-selection rule — is the under-examined methodological choice I’m focusing on.
I compare three rules: closest, which picks the prediction closest to scheduled time; last_before, which picks the last prediction before scheduled time; and latest, which picks the chronologically last prediction available. In this study, latest is treated as the closest GTFS-RT-only proxy for what actually happened.
Hold those three names in your head. We’ll come back to them.
[next slide]
3

## Slide 4
METHOD
Six specification dimensions, fully crossed
Adapting specification-curve and multiverse analysis (Simonsohn et al. 2020; Steegen et al. 2016) to descriptive KPI measurement.
Dimension | Variants | What it controls
Snapshot rule | closest · last_before · latest | Which prediction represents each stop event
Lateness window | 0/+3 · −1/+5 · −2/+7 | Schedule-deviation range counted as on time
Early treatment | count_early_as_late · ignore_early | Whether early arrivals count as failures
Stop selection | all_stops · timepoints · terminals | Which stops contribute to route-level OTP
Time of day | AM peak · midday · PM peak · evening · all | Time window of analysis
Delay basis | arrival · departure | Scheduled time used as the reference
3 × 3 × 2 × 3 × 5 × 2 = 540 specifications per route · 1,080 total across both routes
Notes: Quick word on the framework.
I’m building on specification-curve analysis and multiverse analysis. The basic idea is: instead of computing the metric once with one set of choices, compute it across a structured set of reasonable choices and report the distribution.
I chose six dimensions because each one represents a choice an external analyst has to make when computing OTP from the data.
First is snapshot rule. This is the GTFS-RT-specific choice. Since the feed gives repeated predictions for the same scheduled stop, I need a rule for deciding which prediction represents the stop event.
Second is lateness window. This is the classic OTP definition choice: how many minutes early or late still counts as on time? I test a strict 0 to 3 minute window, a moderate -1 to +5 window, and a wider -2 to +7 window.
Third is early treatment. Early buses are tricky because they may look “not late,” but from a rider perspective, an early bus can be worse than a late bus because you might miss it completely. So I compare counting early arrivals as failures versus ignoring them.
Fourth is stop selection. Some OTP systems measure all stops, while others focus on timepoints or terminals. That matters because endpoint performance may not represent the whole route.
Fifth is time of day. Reliability can differ between AM peak, midday, PM peak, evening, and all-day service, so I include those windows separately.
Sixth is delay basis: arrival versus departure time. In SEPTA’s static GTFS feed, those scheduled times are encoded identically at every stop, so this dimension ends up producing no variation. But I kept it because it is still a real choice in GTFS-based analysis, and the zero result tells us something about the feed.
Crossing those six dimensions gives 540 specifications per route. With two routes, that gives 1,080 total specifications.

## Slide 5
RESULT 1: THE SPREAD
Reasonable choices produce ~80 percentage points of variation
Distribution of OTP across high-sample specifications, 432 per route.
Route 23
79.5 pp
spread of OTP values
MIN
20.3%
MEDIAN
67.0%
MAX
99.8%
the same data · 432 high-sample specs
Route 47
79.0 pp
spread of OTP values
MIN
20.3%
MEDIAN
60.0%
MAX
99.3%
the same data · 432 high-sample specs
Notes: Here’s the final finding.
The full design creates 1,080 total specifications. For the main results, I focus on the high-sample specifications — 864 total, or 432 per route.
For Route 23, OTP ranges from 20.3 percent all the way up to 99.8 percent. The median is 67 percent. That is a 79.5 percentage-point spread.
Route 47 shows almost the same pattern: 20.3 percent at the low end, 99.3 percent at the high end, with a median of 60 percent.
So the same underlying data — the same routes, same agency, same time period — can produce values from about 20 percent on time to almost 100 percent on time.
That does not mean every number is equally useful for every purpose. It means the reported number depends heavily on which reasonable specification was used.
If someone publishes only one OTP number from public GTFS-RT data without disclosing the method, the reader has no way to know which version of the question that number answered.
[next slide]
5

## Slide 6
RESULT 1: THE SPREAD (VISUALIZED)
The specification curve
Each point is one high-sample OTP estimate, sorted from lowest to highest.
TAKEAWAY The 'curve' is the answer. No single point is privileged.
Notes: This is the specification curve.
You do not need to read every tick mark. The point is the overall pattern.
The top panel shows the OTP estimates sorted from lowest to highest. Route 23 is in dark blue, and Route 47 is in gold. The curve starts around 20 percent and rises to almost 100 percent. The dashed lines mark the medians: 67 percent for Route 23 and 60 percent for Route 47.
The bottom panel shows which methodological choices produced those values. The color groups correspond to the main specification dimensions: snapshot rule, lateness window, early treatment, stop selection, and time of day. Delay basis is omitted here because it produces identical values in SEPTA’s data.
If you look at the snapshot-rule group at the top. The closest rule clusters toward the high-OTP side. The latest and last_before rules appear much more on the lower side. That pattern is the snapshot-rule effect made visible.
The lateness window also behaves the way we would expect: stricter windows show up more on the low-OTP side, while wider windows show up more on the high-OTP side.
The key takeaway is that the curve itself is the answer. There is no single privileged point. The reported OTP depends on which path through the specification space the analyst chose.
[next slide]
6

## Slide 7
RESULT 2: PIPELINE CHOICES MATTER
Sensitivity by specification dimension
Mean OTP range when varying each dimension while holding all others fixed.
Chart: 
| Snapshot rule | Lateness window | Early treatment | Stop selection | Time of day | Delay basis
Mean OTP range (pp) | 30.7 | 27.3 | 14.8 | 9.6 | 7.5 | 0
THE FINDING
Snapshot selection is largest
30.7 pp mean range
Largest dimension — even above the well-studied lateness window.
Less visible because it happens upstream during event reconstruction.
Notes: Slide 6 showed the pattern visually. This slide quantifies it.
For each dimension, I held all the other choices fixed and measured how much OTP changed when I varied only that one dimension. Then I averaged across all combinations.
Snapshot selection is the largest source of variation. It produces a mean OTP range of 30.7 percentage points.
That is larger than any other dimension, including the lateness window, which comes second at 27.3 percentage points.
Early treatment comes third at about 15 points. Stop selection is 9.6 points. Time of day is 7.5.
In this case study, stop selection was smaller than I expected, especially because prior work suggests stop sampling can matter for OTP. That does not mean stop selection is unimportant generally. It means that in this GTFS-RT reconstruction setting, snapshot selection moved the KPI more.
Delay basis contributes zero because SEPTA’s static GTFS feed encodes arrival and departure times identically at each stop.
Snapshot selection is the largest source of variation in this case study, and it is less visible than choices like the lateness window because it happens upstream during event reconstruction.
[next slide]
7

## Slide 8
RESULT 3: A CLOSER LOOK AT SNAPSHOT SELECTION
Snapshot selection alone shifts OTP by 30+ percentage points
All other dimensions held fixed at one reference specification (−1/+5 window, count early as late, all stops, all day, arrival).
Snapshot rule | What it does | Route 23 | Route 47
closest | Prediction nearest scheduled time | 87.4% | 86.2%
last_before | Last prediction before scheduled time | 60.7% | 55.9%
latest | Chronologically last prediction (GTFS-RT-only proxy) | 56.0% | 48.8%
WHY THIS HAPPENS — SELECTION BIAS
The closest rule selects the prediction nearest scheduled time. OTP rewards closeness to scheduled time.
The selection rule and the metric measure overlapping properties — the rule biases toward predictions that already look on time.
Notes: This slide takes a closer look at the largest sensitivity dimension: snapshot selection.
The direction of this result is not surprising. If a rule selects the prediction closest to scheduled time, it will tend to produce higher OTP, because OTP itself rewards closeness to scheduled time. I am not treating closest as the recommended reporting rule. I include it as a plausible but outcome-biased reconstruction shortcut.
The important point is the size of the effect. Holding everything else fixed — minus-one to plus-five lateness window, count early as late, all stops, all day, arrival-based delay — changing only the snapshot rule moves Route 23 from 87.4 percent with closest to 56.0 percent with latest. Route 47 moves from 86.2 percent to 48.8 percent.
Same data. Same lateness window. Same stops. Same time period. The only thing that changed is which GTFS-RT prediction represents the stop event.
The takeaway is that the reconstruction step can change the final KPI before the OTP window is even applied.
[next slide]
8

## Slide 9
THE EXTREMES EXPLAINED
Extreme values come from combinations of methodological choices
Neither endpoint is the single 'correct' value — each answers a different question.
THE HIGH END ~ 99%
Specs that produce very high OTP
closest snapshot rule
ignore_early arrivals
wider lateness window (−2/+7)
AM peak only
Morning buses run early in light traffic. Combined with ignore_early, those early arrivals get classified as on-time.
THE LOW END ~ 20%
Specs that produce low OTP
last_before snapshot rule
count_early_as_late
strict 0/+3 lateness window
terminals only
Stricter reconstruction, strict symmetric window, treats early as failure, focuses on high-variability stops on a route.
Notes: One objection is: are the extreme specifications just bugs or edge cases?
I do not think so. They are produced by combinations of individually reasonable choices.
The high-end specifications share a pattern: closest snapshot rule, ignore early arrivals, wider lateness window, and AM peak. Each of those can be defended in isolation. But together, they select strongly for stop events that look on time, producing values near 99 percent.
The low-end specifications have a different pattern: last_before or latest, count early arrivals as failures, strict 0-to-3-minute window, and terminals only. That combines stricter reconstruction with a stricter OTP definition, so it produces values near 20 percent.
Neither endpoint should be treated as “the” correct value. The point is that without disclosure, the reader cannot tell which question the reported OTP number actually answered.
[next slide]
9

## Slide 10
PRACTICAL CONTRIBUTION
Minimum disclosure checklist for GTFS-RT-based OTP
If you publish OTP from public GTFS-RT data, disclose these alongside the number.
Snapshot-selection rule — Often missing
✓
Lateness window — What counts as on time
✓
Early-arrival treatment — Whether early service is a failure
✓
Stop-selection rule — All stops, timepoints, or terminals
✓
Service-date boundary — How midnight-crossing trips are assigned
✓
Trip-matching rule — How real-time updates map to scheduled events
✓
Time period and service filters — Scope of the reported KPI
✓
Sample size — How many observations support the value
✓
Excluded trips/records — Filtering choices (Owl, cancellations)
✓
GTFS-RT feed type and interval — What real-time data is available
✓
Static GTFS version — Schedule benchmark
✓
Notes: So what do we do about this?
The practical contribution is a minimum disclosure checklist for GTFS-RT-based OTP reports.
I would not read all eleven items here. The point is that an OTP number should come with its methodology: lateness window, early-arrival treatment, stop selection, service-date rule, trip matching, sample size, exclusions, feed interval, and GTFS version.
In the GTFS-RT performance work I reviewed, this choice was usually treated as a pipeline detail rather than highlighted as part of the reported KPI methodology.
But in my results, it was the largest source of variation.
So the practical recommendation is simple: if you publish OTP from public GTFS-RT data, disclose how stop events were reconstructed, not just what lateness window you used.
[next slide]
10

## Slide 11
SCOPE AND NEXT STEPS
Limitations & future work
LIMITATIONS
Two routes, one agency
Routes 23 and 47, SEPTA. Magnitudes may differ across feeds.
Three weeks of data
Apr 4 to Apr 25, 2026. Weekday day-service only.
No AVL ground truth
latest is treated as the closest GTFS-RT-only proxy for actual arrivals — but it remains a proxy.
Six dimensions, not all
Trip matching, missing-data thresholds, weekend/Owl scope could matter.
OTP, not headway
For high-frequency service, headway regularity may better represent rider experience.
FUTURE WORK
Cross-agency comparison
Does the snapshot-rule effect generalize beyond SEPTA?
AVL ground-truth comparison
Which GTFS-RT reconstruction rule best approximates actual arrivals?
Headway-based reliability
Apply the same robustness protocol to high-frequency service metrics.
Dashboard/reporting interface
Interactive visualization of the spec curve and disclosure choices.
Reproducible pipeline
Public GitHub repo: tobibussiek/TransitKPIFramework
Notes: A few limitations.
This is two routes, one agency, and about three weeks of data. I cannot claim the exact magnitudes generalize to every transit system.
I also do not have SEPTA’s internal AVL data, so I cannot validate latest against ground truth. It is a GTFS-RT-only proxy.
And the project focuses on OTP, even though for high-frequency service, headway regularity may better represent rider experience.
Future work would be a cross-agency comparison, a GTFS-RT versus AVL ground-truth comparison, and applying the same robustness protocol to headway-based reliability.
A final extension would be a dashboard or reporting interface that lets users explore the specification curve interactively.
[next slide]
11

## Slide 12
THANK YOU
Questions?
OTP cannot be reported as a single unqualified number when computed from public GTFS-RT data.
Disclose how stop events were reconstructed, how on-time was defined, and how sensitive the result is to reasonable alternatives.
Tobias Bussiek
West Chester University of Pennsylvania · M.S. Computer Science
github.com/tobibussiek/TransitKPIFramework
Notes: That’s the talk.
The bottom line is simple: OTP from public GTFS-RT should not be reported as a single unqualified number.
Disclose how stop events were reconstructed. Disclose how “on time” was defined. And show how sensitive the result is to reasonable alternatives.
Thank you — I’m happy to take questions.
12